## Slide 1: CyberSkills2Work The National Cybersecurity Workforce Development Program

## Slide 2: Industrial Control Systems Security
This program is funded by the National Security Agency National Centers of Academic Excellence in Cybersecurity (NCAE-C) Program.
For additional information, please visit www.CyberSkills2Work.org.
Acknowledgement
Course Title
CRN
©2024 CyberSkills2Work - Institution Name

## Slide 3: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
How ICS risks differ from traditional IT
Defining Cybersecurity risk, with special emphasis on ICS
Identifying Assets
Patching Systems
Risk Assessment formulas
Risk Assessment step
Threat Modeling
Case Study
Risk Assessment Lab
Overview
Notes: Briefly discuss the content covered in this module.

## Slide 4: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
ICS integrates computer networks with physical equipment
Creates cybersecurity risks beyond financial loss
Safety, environment, and business continuity at stake
Requires tailored risk assessments—different from IT
Based on standards like ISA/IEC 62443, NIST 800-82, Rev 3, and CISA Risk Guidance
Introduction to ICS Risk Management and Assessments
Notes: Instructor Notes:
ICS systems aren’t just data processors—they interact with the real world. Unlike IT systems, a cyberattack on ICS could spill chemicals, overheat machinery, or disable safety systems. This reality makes risk management not just a compliance activity, but a foundational pillar of industrial safety and reliability. Set the stage for risk as both a technical and strategic business concern.
In Industrial Control Systems (ICS), a risk assessment is a process that evaluates the potential for cyberattacks and other threats, and helps organizations identify and prioritize vulnerabilities and risks. The goal is to understand the potential impact of cyberattacks, develop effective security measures, and create a plan to mitigate identified risks.
Key aspects of an ICS risk assessment include:
Identifying assets and critical functions:
This involves understanding which systems and components are crucial for the operation of the ICS.
Assessing threats and vulnerabilities:
Identifying potential threats, such as malware, insider threats, and third-party risks, and evaluating vulnerabilities in the ICS environment.
Analyzing the impact of threats:
Determining the potential consequences of a cyberattack, including financial losses, operational disruption, and safety risks.
Prioritizing risks:
Identifying which risks pose the greatest threat and require immediate attention.
Developing mitigation strategies:
Creating plans to prevent, detect, and respond to cyberattacks, including security controls, incident response procedures, and training programs.
Implementing and monitoring security measures:
Putting security measures in place and continuously monitoring their effectiveness.
Benefits of an ICS risk assessment:
Improved cybersecurity posture:
By identifying and addressing vulnerabilities, organizations can reduce their risk of cyberattacks.
Reduced downtime and operational disruption:
With proactive risk mitigation, organizations can minimize the impact of cyberattacks on their operations.
Compliance with regulatory requirements:
Many regulatory bodies require organizations to implement ICS security measures, and a risk assessment can help demonstrate compliance.
Cost-effective security investments:
A risk assessment can help organizations prioritize security investments and allocate resources efficiently.
NOTE: Vulnerability and Risk are not the same thing. A vulnerability is a weakness or flaw that can be exploited, while risk is the potential for loss or damage that could result from that exploitation.

## Slide 5: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
ICS risks can involve:
Loss of containment
Environmental damage
Injury or death
Economic and reputational harm
Safety Instrumented Systems (SIS) can be targeted
Cyber events may be latent—waiting for an initiating condition
Why ICS Cyber Risk is Different
Notes: Instructor Notes:
Emphasize how an attacker might disable protective systems rather than cause direct damage—e.g., change a pressure trip point, then wait for a process deviation. This indirect method mirrors Triton/TRISIS. Teach students to think beyond conventional IT incident models. SIS (Safety Instrumented System) and DCS coordination failures can be catastrophic.
Note on SIS :
SIS systems operate independently from the main process control systems (like DCS) to ensure they remain functional even if the main control system fails.
SIS is designed to take action only when a hazardous condition is detected, while DCS systems continuously monitor and control the process during normal operations.
SIS systems are often referred to by other names, such as Emergency Shutdown System (ESD), Safety Shutdown System, or Safety Interlock System
SIS Components:
* a sensor, which monitors the process to detect an upset or abnormal condition (for example, a pressure sensor)
• a logic device which receives the signal from the sensor, determines if the condition is hazardous, and, if so, sends a signal to take action.
• a final control device, which receives the signal from the logic device and implements the appropriate action in the plant (for example, opening or closing a valve, shutting down a pump)
There are also different Safey Integrity Levels (SILs), where each level deals with varying levels of risk. The higher the SIL, the more redundancy is necessary to deal with the risk.
Key players include ABB, Emerson, Honeywell, Rockwell Automation, Schneider Electric, Yokogawa, and Siemens. For example, Emerson has the DeltaV SIS
------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
ICS cyber risk is different from traditional IT cyber risk primarily due to the criticality of the systems, the potential for physical harm, and the unique challenges of legacy technology and operational needs. Unlike IT systems, which focus on protecting data, ICS prioritize safety, availability, and integrity of critical processes, making cyberattacks potentially catastrophic.
Here's a more detailed breakdown:
Criticality and Physical Impact:
ICS often control critical infrastructure like power grids, water treatment plants, and manufacturing facilities. A cyberattack on these systems can have immediate and severe physical consequences, including loss of life, injuries, and widespread damage.
Legacy Technology and Maintenance:
Many ICS systems are decades old and lack modern security features, making them vulnerable to outdated and sophisticated attacks. Furthermore, maintaining these systems often requires long downtime, making security updates and patching challenging.
Operational Needs and Downtime Tolerance:
ICS environments are designed for continuous operation, with minimal tolerance for downtime. This makes it difficult to implement security measures that might require shutting down systems for updates or maintenance.
Fragmented Ownership and Communication:
IT and OT (Operational Technology) teams often operate in silos, leading to miscommunication and gaps in security coverage.
Different Threat Landscape:
ICS are increasingly targeted by state-sponsored actors, hacktivists, and cybercriminals, who see them as valuable targets for disruption and sabotage.
Risk Priorities:
While IT security prioritizes confidentiality, integrity, and availability, ICS security places safety and availability at the forefront.

## Slide 6: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Cyber risk = threats × vulnerabilities × target impact
Threats can be:
Intentional (e.g., APT, insider)
Unintentional (e.g., operator error)
Consequences depend on:
Asset criticality
Hazardous potential
System compromise depth
Defining Cybersecurity Risk
Notes: Instructor Notes:
In industrial contexts, attractiveness isn't about data—it’s about what physical outcomes an adversary can cause. For instance, a chlorine valve at a water facility is highly attractive. Let’s look at the Risk Assessment formula in greater detail.
1. Define the Risk Equation
Cybersecurity Risk = Threat X Vulnerability X Impact
This formula is multiplicative—if any one factor is zero, the overall risk is effectively null. But in practice, we use scoring scales (e.g., 1–5 or 1–10) to normalize subjective assessments.
2. Define the Components
Threat: The presence and capability of an adversary to exploit a system.
  Example scale:
    1 = Low threat (no known actors targeting)
    5 = High threat (known APT activity)
Vulnerability: Weaknesses in the system that could be exploited.
  Example scale:
    1 = Hardened system, strong controls
    5 = Unpatched, exposed, or default configurations
Impact: The consequence if the threat is realized.
  Categories: Safety, Environmental, Financial, Operational
  Example scale:
    1 = Negligible (e.g., minor report delay)
    5 = Catastrophic (e.g., explosion, loss of life)
3. Step-by-Step Scenario
Example System: A PLC that controls a chemical dosing valve in a water treatment plant.
Threat Rating: 4
  APT29 has targeted regional utilities, including water facilities. We will discuss APTs and MITREs ATT&CK MATRIX in detail during Module 07 – Threats to ICS. ***Optional: show students MITRE’s ATT&CK MATRIX briefly.
Vulnerability Rating: 5
  PLC has default credentials, directly accessible via flat network.
Impact Rating: 5
  Overdosing chemicals could poison drinking water, causing a public health emergency.
Calculation:
Risk Score=4(Threat)×5(Vulnerability)×5(Impact)=100 {Risk Score}. On a scale of 0–125 (max 5×5×5), this is a very high/critical risk score.
4. Interpretation
The PLC must be prioritized for mitigation.
Mitigations could include:
  Changing default credentials
  Network segmentation
  Remote access logging and monitoring
  Applying firmware updates or compensating controls
5. Bonus: Adjusted Risk After Controls
If mitigations reduce vulnerability from 5 to 2:
New Risk Score=4×2×5=40. This shifts the risk from critical to moderate, possibly within the organization's risk tolerance threshold. However, it should be noted that a moderate score in ICS is still not ideal.
Possible outcomes of a moderate risk in ICS:
Service disruptions: Production pauses or delays.
Equipment damage: Malicious manipulation of control commands could cause equipment damage.
Safety concerns: Compromised systems could lead to unsafe conditions or accidents.
Financial losses: Downtime, repair costs, and potential legal fees.

## Slide 7: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Expanded Scope: Now covers a broader range of Operational Technology (OT), not just Industrial Control Systems (ICS).
Focus on OT Security: Provides guidance on securing OT systems with their specific performance, reliability, and safety needs.
Risk Management: Emphasizes risk management for OT, including hazard analysis.
Cybersecurity Framework Alignment: Aligns with the NIST Cybersecurity Framework for a unified approach.
Incident Response: Provides detailed guidance for OT incident response and recovery.
Supply Chain Security: Addresses supply chain risks related to OT.
Security Controls: Offers specific security controls and countermeasures for OT systems.
Defense-in-Depth: Promotes a layered security approach.
Continuous Monitoring: Highlights the need for real-time OT monitoring and threat intelligence.
Tailoring Guidance: Includes new guidance for tailoring NIST SP 800-53 Revision 5 controls for OT.
Updated Threats and Vulnerabilities: Includes updates on OT threats and vulnerabilities.
NIST 800-82, Rev. 3
Notes: Instructor Notes:
NIST SP 800-82 Revision 3 is a key publication titled:
“Guide to Operational Technology (OT) Security”, published by NIST in February 2023. It replaces earlier versions that focused specifically on Industrial Control Systems (ICS). Rev. 3 expands the focus to encompass all forms of OT, including:
Industrial Control Systems (ICS)
Distributed Control Systems (DCS)
Supervisory Control and Data Acquisition (SCADA)
Building Automation Systems (BAS)
Safety Instrumented Systems (SIS)
Other OT systems used in manufacturing, utilities, transportation, etc.
Core Features of NIST SP 800-82, Rev. 3
Purpose
Provide guidance on improving security for OT environments while maintaining safety and reliability.
Bridge the gap between IT security practices and OT operational requirements.

## Slide 8
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
NIST 800-82, Rev. 3 Key Enhancements
Area | Description
Expanded Scope | Covers a broader set of OT systems beyond traditional ICS.
Risk Management Alignment | Integrates with NIST RMF (SP 800-37) and Cybersecurity Framework (CSF).
Threat Intelligence Integration | Acknowledges evolving threats (e.g., ransomware, TRISIS, supply chain attacks).
Asset Categorization | Suggests methods for classifying OT assets by criticality and function.
Security Architecture | Emphasizes network segmentation, zero trust, and Purdue Model alignment.
Security Controls | Maps NIST SP 800-53 controls for OT applicability.
Operational Constraints | Balances security measures with availability and real-time process needs.
Notes: Instructor Notes:
Core Security Principles for OT (per 800-82 Rev. 3)
Know Your Assets Build and maintain an accurate inventory of all OT devices and software.
Segment Networks Limit communications between zones, especially between enterprise IT and OT. This is considered a near-requirement, meaning some jurisdictions implement legal standards for segmentation, but not all.
Implement Least Privilege Limit user and service access based on functional necessity.
Monitor and Detect Anomalies Use OT-aware IDS, log analysis, and continuous monitoring.
Manage Patching and Vulnerabilities Apply updates with careful testing to avoid process disruptions. **** Changes to an ICS system could include device firmware updates, embedded hardware upgrades and/or replacements, setpoint changes ( whichrefers to the modification of the desired target value (setpoint) for a process variable, such as temperature, pressure, or flow rate), instrumentation calibrations, controller logic changes, and software patches. Patches should be made during a scheduled engineering maintenance window.
Plan for Incident Response Have OT-specific playbooks and recovery procedures in place.
Conduct Risk Assessments and Threat Models
Use in ICS Risk Assessments
Provides a control framework and assessment methodology for evaluating ICS/OT environments.
Facilitates risk scoring, mitigation strategies, and compliance validation.
Supports alignment with IEC 62443, CISA guidance, and sector-specific standards.

## Slide 9: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Identifying Risks: Understanding potential threats, vulnerabilities, and their impact on an organization's assets.
Assessing Impact and Likelihood: Evaluating the potential consequences of a successful cyberattack.
Managing Risks: Implementing controls and strategies to mitigate identified risks.
Systemic Risk Reduction: Focusing on addressing vulnerabilities that could have a broader impact on critical infrastructure.
Cybersecurity Best Practices: CISA provides guidance on implementing best practices to enhance cybersecurity posture.
CISA ICS Risk Assessment Guidance
Notes: Instructor Notes:
Link to CISA’s Guide to Getting Started with a Cybersecurity Risk Assessment: https://www.cisa.gov/sites/default/files/2024-09/24_0828_safecom_guide_getting_started_cybersecurity_assessment_2022_final_508C.pdf

## Slide 10: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Identify system under consideration (SUC)
System screening (connectivity, programmability)
Determine worst-case consequence
Identify threat vectors and likelihood
Apply countermeasures and assign SL-T
Confirm tolerable risk is met
ISA/IEC 62443, Part2-1 Risk Assessment Steps
Notes: Instructor Notes:
ISA/IEC 62443, Part 2-1 outlines a rigorous, repeatable process for performing cybersecurity risk assessments tailored to industrial automation and control systems (IACS). This methodology ensures that zones and conduits are evaluated in context, and appropriate Security Level Targets (SL-T) are assigned.
This involves a structured approach to identifying, analyzing, and mitigating cybersecurity risks in industrial automation and control systems (IACS). It typically includes defining the scope, identifying threats and vulnerabilities, analyzing potential impacts, prioritizing risks, and documenting the findings. This process is a continuous lifecycle that includes phases like Assess, Develop and Implement, and Maintain, according to ISA/IEC 62443
NOTE: The ISA/IEC 62443 Standards document is very expensive, like $350.00 USD expensive.

## Slide 11: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
SUC: Define scope—zone, conduit, or full system
Clarify network boundaries
Use zone/conduit diagrams to structure assessment
Focus may be one zone (e.g., SIS), or full control network
Identify the System Under Consideration (SUC)
Notes: Instructor Notes:
Step 1: Identify the System Under Consideration (SUC)
What it means:
Define the scope of the assessment.
Identify and document the assets, zones, and conduits that will be evaluated.
SUC can be:
  An entire plant network
  A safety system (SIS)
  A PLC/RTU subsystem
  An individual zone (e.g., control room network)
Why it matters:
Clear scoping avoids overlooking components or over-extending analysis.
Ensures that assessment resources are focused on relevant systems.
Example:
Assessing the security of an engineering workstation (EWS) used to program PLCs within a Safety Instrumented System (SIS) zone.

## Slide 12: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Programmability (e.g., PLCs, engineering stations)
Use of portable/removable media
OT network connectivity
Non-OT network exposure (e.g., VPN, cloud)
System Screening Factors
Notes: Instructor Notes:
Step 2: Perform System Screening
What it means:
Analyze each asset within the SUC based on exposure and criticality:
  Degree of programmability (can it change process logic?)
  Use of removable media or portable computers
  OT network connectivity (to L1, L2, L3)
  External connectivity (L4 corporate, internet, VPN)
Why it matters:
Prioritizes high-risk, high-impact nodes for further analysis.
Focuses effort on devices with high attack surface.
Example:
An operator HMI with USB ports, always connected to the PCN and L3.5 (Process Control Access Domain), is a higher-risk node than a read-only historian server.

## Slide 13: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Assess impact if system is:
Powered down for days
Fully compromised by skilled actor
Consider:
Safety
Environmental
Financial impact
Ignore countermeasures at this stage
Determining Worst-Case Consequences
Notes: Instructor Notes:
Step 3: Determine the Worst-Case Consequences
What it means:
Analyze what could happen if an asset were compromised, ignoring all cyber protections.
Focus on unmitigated outcomes—assume:
  Firewalls fail
  Antivirus disabled
  No access control
Consequence Categories:
Health and Safety (H&S)
Environmental (e.g., spills, emissions)
Financial (e.g., downtime, product loss)
Reputational
Regulatory
Why it matters:
Establishes the baseline impact.
Guides later decisions about what level of protection is “good enough.”
Example:
If a PLC in a chlorine dosing system is hacked and causes chemical over-injection, the worst-case consequence could be public poisoning and regulatory fines.

## Slide 14: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Use a structured matrix:
Severity (e.g., 1–5)
Categories (H&S, financial, environmental)
Matrix aligns with corporate risk tolerance
Consequence Evaluation
Notes: Instructor Notes:
Consequence evaluation in Industrial Control Systems (ICS) focuses on assessing the potential impact of cybersecurity threats on critical functions and processes. This process helps organizations understand the potential harm a breach could cause, ranging from process disruptions to safety incidents, and informs risk management decisions.
1. Understanding the Importance of Consequence Evaluation:
Impact on Critical Functions:
ICS systems are vital for various industries, and cyberattacks can have significant consequences for processes, production, and safety.
Risk Management:
Consequence evaluation is a crucial part of ICS risk assessments, helping organizations prioritize threats and vulnerabilities based on their potential impact.
Defense Strategies:
Understanding the potential consequences of attacks helps organizations develop effective cybersecurity defenses, including incident response plans.
2. Methods for Evaluating Consequences:
Consequence-Driven Cyber-informed Engineering (CCE):
This methodology, developed by Idaho National Laboratory (.gov), helps identify critical functions and assess the impact of potential attacks.
Crown Jewel Analysis:
This approach focuses on identifying the most critical assets within an ICS environment and evaluating the consequences of their compromise, according to Dragos.
Functional Impact Analysis:
This involves analyzing how different ICS functionalities might be affected by an attack, such as process disruptions, safety violations, or economic losses.
3. Tools and Techniques for Consequence Evaluation:
Phased Analysis:
This involves breaking down the ICS into various stages and identifying the impact of attacks at each stage.
Worst-Case Scenario Analysis:
This involves identifying the most severe possible consequences of an attack to help organizations prepare for the worst.
Risk Assessment Frameworks:
Various risk assessment frameworks, such as those from ISA Global Cybersecurity Alliance, can be used to evaluate the consequences of attacks.

## Slide 15: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Physical access (USB, console, rogue device)
Remote access (VPN, serial, cloud, PCAD)
Network pivoting
Wireless or removable media attacks
Based on:
Threat actor sophistication
Access pathway complexity
Target value
Done without assuming current mitigations
Identify Threat Vectors & Assess Likelihood
Notes: Instructor Notes:
Step 4: Identify Threat Vectors and Assess Likelihood
What it means:
Document how threats could reach the system:
  Physical access (USB, rogue device, console)
  Network pathways (VPN, L3 bridge, insecure Wi-Fi)
  Human factors (insiders, phishing)
Evaluate likelihood of initiating events:
  Skill required
  Ease of access
  Known threat actor presence
Why it matters:
Helps prioritize risks.
Builds an “attack path” understanding aligned with MITRE ATT&CK for ICS.
Example:
An engineering station connected to both L3 (control) and L4 (business) is vulnerable to remote access threats. Likelihood is “high” due to flat network and weak authentication.

## Slide 16: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
SL-T = Target Security Level (0–4)
Determined by:
Risk matrix results
Unmitigated risk
Examples:
SL1: Basic integrity
SL4: State-level threat resistance
Countermeasures and SL-T
Notes: Instructor Notes:
Step 5: Identify and Evaluate Countermeasures + Determine SL-T
What it means:
Compare unmitigated risk against corporate tolerability thresholds.
Assign a Target Security Level (SL-T):
  SL0: No cybersecurity required
  SL1: Protect against casual or coincidental violation
  SL2: Against intentional violation by low-skill attackers
  SL3: Against sophisticated threats with moderate resources
  SL4: Against highly sophisticated threats (e.g., nation-states)
Map countermeasures to the specific threat vector:
  Preventive: Firewalls, MFA, access control
  Detective: Logs, IDS
  Mitigative: Process alarms, operator intervention
Why it matters:
Helps define where defenses should be added or improved.
SL-T becomes a key requirement for the zone or conduit.
Example:
If the SL-T for the SIS zone is SL3 but the current environment supports only SL1, additional firewalls, MFA, and activity monitoring are needed.

## Slide 17: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Inherent risk: After accounting for internal systems (e.g., DCS, SIS)
Tolerable risk: After adding external controls (e.g., firewalls, training)
Goal: LOPA gap = 0
Assess Inherent and Intolerable Risk
Notes: Instructor Notes:
Step 6: Assess Inherent and Tolerable Risk
Inherent Risk:
Remaining risk after accounting for built-in safety controls (e.g., DCS alarms, SIS shutdowns, PSV valves).
May reduce the LOPA gap (Layers of Protection Analysis) by 1 or more.
Tolerable Risk:
Remaining risk after applying cyber controls (e.g., segmentation, access policies, anomaly detection).
If the risk ≤ tolerable threshold, no further action required.
If not, redesign architecture, reconfigure assets, or add defenses.
Why it matters:
Final check: is the zone/system acceptable under your risk matrix?
Drives final security design and documentation.
Example:
A compromised PLC causes a chemical spill, but SIS activates to prevent overflow. One LOPA credit reduces the consequence severity score. Adding a data diode reduces threat vector likelihood, making overall risk tolerable.

## Slide 18: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Summary of ISA/IEC 62433 Risk Process
Step | Objective | Output
1. Identify SUC | Define scope | Zone/conduit boundaries
2. Screen System | Prioritize nodes | Risk scoring candidates
3. Worst-Case Consequences | Understand impact | Severity levels
4. Threat Vectors | Map attack paths | Likelihood scores
5. Countermeasures + SL-T | Define needed security | SL-T for zones
6. Tolerable Risk | Final assessment | Action/no action
Notes: Instructor Notes:
Step 6: Assess Inherent and Tolerable Risk
Inherent Risk:
Remaining risk after accounting for built-in safety controls (e.g., DCS alarms, SIS shutdowns, PSV valves).
May reduce the LOPA gap (Layers of Protection Analysis) by 1 or more.
Tolerable Risk:
Remaining risk after applying cyber controls (e.g., segmentation, access policies, anomaly detection).
If the risk ≤ tolerable threshold, no further action required.
If not, redesign architecture, reconfigure assets, or add defenses.
Why it matters:
Final check: is the zone/system acceptable under your risk matrix?
Drives final security design and documentation.
Example:
A compromised PLC causes a chemical spill, but SIS activates to prevent overflow. One LOPA credit reduces the consequence severity score. Adding a data diode reduces threat vector likelihood, making overall risk tolerable.

## Slide 19: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Propose technical and procedural controls
Align with NIST, ISA/IEC 62443, or other frameworks
Prioritize actions based on risk reduction
Risk Mitigation
Notes: Instructor Notes:
Highlight which risks are critical (e.g., unsegmented networks, legacy systems with known CVEs).
Use a risk matrix heatmap to visualize results.
Prioritize based on mission-criticality—some moderate-risk issues might become high-priority if they impact essential control functions.
Focus on both quick wins and long-term controls (e.g., patch management vs. network segmentation).
Include framework alignment: e.g., NIST 800-82 Rev. 3, CIS Controls for ICS, or IEC 62443-3-2.
Include a column for resource estimates or implementation difficulty to guide prioritization.

## Slide 20: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Threat modeling helps visualize how cyberattacks unfold in ICS environments
Goes beyond vulnerability scans—focuses on attacker behaviors, paths, and outcomes
Goal: anticipate, prioritize, and mitigate specific cyber-physical threats
Emphasizes understanding of impact, not just likelihood
Techniques include attack graphs, Petri nets, expert models, and adversarial games
Introduction to Threat Modeling for Risk Assessments
Notes: Instructor Notes:
Threat modeling in ICS is not a checklist—it’s a mental simulation of how an adversary could reach and impact a control process. Unlike traditional IT systems, ICS threat modeling must incorporate physical outcomes, legacy technology, deterministic processes, and operator behaviors. This step often informs the design of zone-based protections and ICS-specific detection logic. Begin by introducing why traditional STRIDE/IT threat models must evolve to address kinetic impact and real-world safety risk.

## Slide 21: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Built using SME (Subject Matter Expert) input and documentation
Maps network resources, data flows, vulnerabilities, and mission relevance
Semi-quantitative estimates: likelihood × consequence
Suitable for legacy networks with limited telemetry
Used to prioritize risk mitigation investments
Expert-Elicited Risk Models
Notes: Instructor Notes:
Expert-elicited models are ideal for ICS environments where real-time data is sparse, and institutional knowledge is rich. The process begins with identifying all relevant assets and flows—e.g., HMI to PLC to actuator—and then consulting operators, engineers, and analysts about their criticality and exposure. Outputs are often spreadsheet-based, combining scores to yield actionable priorities. The real value lies in its ability to rapidly produce usable risk scores without invasive data collection.

## Slide 22: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Attack graphs visualize multiple attack paths across a system
Nodes = system states; Edges = attacker transitions
Identify chokepoints, privilege escalations, pivot opportunities
Adversarial games simulate attacker-defender strategies
Useful for designing proactive defenses and adaptive policies
Attack Graphs and Game-Based Modeling
Notes: Instructor Notes:
Attack graphs model potential sequences of actions an attacker can take, including lateral movement and privilege escalation. For example, a phishing email leads to a compromised operator PC, which then accesses engineering workstation software. Game-theoretic approaches treat attackers and defenders as rational agents—each trying to optimize success versus detection. These tools support “what if” analysis for scenarios like ransomware versus targeted sabotage.
Attack graphs also help visualize how a breach could escalate—e.g., from VPN access, to historian pivot, to PLC command execution. Each node represents a system state.. Use this to plan IR playbooks or justify capital investments.

## Slide 23: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Notes: Instructor Notes:

## Slide 24: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Petri nets model system behavior using transitions and states
Can capture both cyber events and physical process changes
Supports quantitative reachability and impact analysis
Effective for modeling complex multi-stage attacks (e.g., Stuxnet)
Used for scenario-based planning and mitigation backtracking
Petri-Net Threat Models
Notes: Instructor Notes:
Petri nets allow analysts to simulate the progression of attacks alongside the effects on ICS processes. They can model the timing and dependencies of actions (e.g., logic changes in PLCs triggering unsafe tank levels). This formalism supports risk quantification by computing “reachable” states—i.e., what states the system can evolve into from an initial compromise. Petri nets are powerful for identifying combinations of actions that might not appear risky in isolation but are dangerous together.
Here are the details:
Places (P): Represent states or conditions within the system.
Transitions (T): Represent events or actions that can occur.
Arcs (F): Show the flow of control and data between places and transitions.
How Petri Nets are Used in ICS Threat Modeling:
Modeling ICS Dynamics: Petri nets can model the discrete and continuous processes within an ICS, including communication flows, system states, and interactions between components.
Representing Cyberattacks: Attacks can be represented as sequences of transitions that change the system state in a malicious way.
Analyzing System Behavior under Attack: By simulating the Petri net model, one can observe how attacks propagate and impact the system's availability, production rate, and resilience.

## Slide 25: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
A hypothetical manufacturing factory with multiple interconnected stations controlled by an ICS
Petri-Net Elements (represent states)
Attack Modeling (introduces transitions representing attacker actions)
Resilience Analysis (introduces transitions representing cyber responses)
Example Flow (Simplified)
Petri-Net Scenario
Notes: Instructor Notes:
Petri Net Elements:
Places: Represent states like "Normal Operation," "Cyber Attack Detected," "Station 1 Offline," "Production Rate Decreased," "Mitigation Applied," etc.
Transitions: Represent events like "Attack on PLC," "Detection of Anomalous Traffic," "Stopping of Station 1," "Recovery Process Initiated," etc.
Arcs: Connect places and transitions to show the sequence of events and their consequences. For instance, an arc from "Attack on PLC" to "Station 1 Offline" indicates that the attack leads to the station being taken offline.
Attack Modeling:
Malicious Transitions: Introduce transitions representing attacker actions, such as exploiting a vulnerability in a Programmable Logic Controller (PLC).
Attack Propagation: Model how the attack spreads through the ICS network, potentially affecting other stations or systems.
Simultaneous Attacks: Petri nets can represent coordinated attacks involving multiple attacker actions occurring concurrently.
Resilience Analysis:
Modeling Mitigation: Introduce transitions representing cybersecurity responses, like isolating infected devices or applying patches.
Recovery Processes: Model the system's ability to recover from the attack and resume normal operations.
Resilience Curves: Generate "resilience curves" by simulating the model, which show the system's availability or production rate over time during an attack and subsequent recovery.
Example Flow (Simplified):
Normal Operation (Place): System is functioning as expected.
Attack on PLC (Transition): An attacker successfully compromises a PLC.
PLC Compromised (Place): The PLC is now under attacker control.
Station 1 Offline (Transition): The attacker shuts down Station 1 through the compromised PLC.
Production Rate Decreased (Place): The production rate is affected by Station 1 being offline.
Detection of Anomalous Traffic (Transition): The security system detects unusual network activity.
Cyber Attack Detected (Place): The attack is identified.
Mitigation Applied (Transition): Response actions are taken, such as isolating the compromised PLC.
Station 1 Restored (Transition): Station 1 is brought back online after mitigation.
Normal Operation (Place): The system returns to a normal state

## Slide 26: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Petri-Net Example
Notes: Instructor Notes:
Example of a Petri-Net

## Slide 27: Module 06 – Risk Assessments in ICS
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
ICS Risk Assessment Reports
Understanding the organization and its assets:
Identifying risks and vulnerabilities:
Establishing the probability of risks and frequency of events:
Determining impacts:
Developing mitigation strategies:
Considering options
Performing a cost-benefit analysis:
Notes: Instructor Notes:
Understanding the organization and its assets: This involves mapping out the interconnectedness of people, assets, and processes within the ICS environment.
Identifying risks and vulnerabilities: This involves identifying weaknesses in policies, procedures, platforms, and networks that could be exploited. This can be done by reviewing technical documentation, performing physical inspections, and conducting interviews with personnel.
Establishing the probability of risks and frequency of events: This involves assessing the likelihood of identified threats materializing.
Determining impacts: This involves calculating the potential consequences of a security incident, which can range from financial losses to environmental damage and even harm to human life.
Developing mitigation strategies: This involves outlining measures to prevent or reduce the impact of identified risks.
Considering options: This involves evaluating different mitigation approaches.
Performing a cost-benefit analysis: This involves assessing the financial implications of implementing different mitigation strategies

## Slide 28: Module 06 – ICS Risk Assessment
Course Title
CRN
©2021 CyberSkills2Work - Institution Name
Lab and CISA Certs
Lab 6 – Risk Assessment Handout
Link Provided By Instructor
CISA ICS Cert (210W-5)
https://www.cisa.gov/resources-tools/programs/ics-training-available-through-cisa
Notes: Instructor Notes:
Please complete Lab 6 before next week’s Module. A link to The Risk Assessment report and instructions will be provided to students.